MAD  DATA


INTRODUCTION

The Index Properties data file contains information generated 
onboard the JOIDES Resolution by the shipboard physical 
properties scientists and technicians.  Each sample is placed 
in a numbered beaker and is weighed on a balance, and the 
volume of the sample and beaker is measured in a pycnometer.  
The sample is then dried and the weight and volume are 
remeasured.  The index properties are calculated from these 
values.  The balances used to weigh the samples have a 
precision of approximately +/- 0.02 to 0.03 gram, and the 
pycnometers are precise to approximately +/- 0.05 cubic 
centimeter.  This yields a precision of approximately
+/- 1% on unconsolidated sediments and about +/- 2% on 
consolidated sediments
and hard rocks.

The Index Properties data file contains calculated values for 
the Index Properties tests. The calculated values included in 
this data file are wet and dry bulk density, porosity, and 
grain density as well as intermediate calculation 
values, and formulas.


BIBLIOGRAPHY

Boyce, R.E., 1976. Definitions and laboratory techniques of 
compressional sound velocity parameters and water-wet 
content, wet-bulk density, and porosity parameters by 
gravimetric and gamma ray attenuation techniques. In: 
Schlanger, S.O., et al., 1976, Initial Reports of the Deep 
Sea Drilling Project, vol. 33: Washington (U.S. Goverment 
Printing Office) pp. 931-958.


EXPLANATION OF DATA ITEMS

LEG - Number identifying the cruise.  The Ocean Drilling 
Program started numbering the cruises of the JOIDES 
Resolution at Leg 101.

SITE - Number identifying the site.  A site is the position 
of a beacon around which holes are drilled.

HOLE - Letter identifying the hole.

CORE - Number identifying the core.  Cores are numbered 
serially from the top of the hole downward.

CORETYPE - A letter code identifying the drill bit/coring 
method used to retrieve the core.  Coretype codes are:
          B - Drill Bit
          C - Center Bit
          D - Positive Displacement
          H - Hydraulic (Advanced) Piston Core
          I - Interstitial water (only used on Legs 101 to 116)
          M - Miscellaneous
          N - Downhole Mud Motor (Navidrill)
          P - Pressure Core Barrel
          R - Rotary
          S - Side Wall Core
          W - Wash Core
          X - Extended Core Barrel

SECTION - A core is cut into 1.5-meter-long sections that are 
numbered serially from the top of the core.  A core with full 
recovery will have 7 sections and a core catcher and be 
approximately 9.8 meters long.

TOP_INTERVAL - The location in centimeters within a section 
of the top of the interval tested.

BOTTOM_INTERVAL - The location in centimeters within a 
section at the bottom of the interval tested.

SUB_BOTTOM_DEPTH - Depth in meters down the hole from which 
the sample was taken.

BULK_DENSITY - The bulk density of the sample as calculated 
by the dry pycnometer volume method in grams/cubic 
centimeter.

DRY_DENSITY - The dry density of the sample as calculated 
by the dry pycnometer volume method in grams/cubic 
centimeter.

GRAIN_DENSITY - The grain density of the sample as 
calculated by the dry pycnometer volume method in grams/cubic 
centimeter.

POROSITY - The porosity of the sample as calculated by the 
dry pycnometer volume method as a percentage.