GAMMA RAY ATTENUATION POROSITY EVALUATION (GRAPE) DATA 


INTRODUCTION

The Gamma Ray Attenuation Porosity Evaluation (GRAPE) data 
files contains information generated onboard JOIDES 
Resolution by the shipboard physical properties scientists 
and technicians. Each whole round core section is moved along 
a horizontal Multi-Sensor Track (MST) where successive 
intervals are continuously bombarded by a beam of radiation. 
Gamma rays which transmit through the entire core are 
detected and counted. The amount of gamma radiation 
transmitted through the core is inversely proportional to the 
bulk density of the rock or sediment.

The GRAPE data files represent measurements obtained from all 
cores from a given hole. Each record in the data file 
represents a density/porosity evaluation measurement at a 
given point in the whole round core.


BIBLIOGRAPHY

Boyce, R.E., 1976. Definitions and laboratory techniques of 
compressional sound velocity parameters and water-wet 
content, wet-bulk density, and porosity parameters by 
gravimetric and gamma ray attenuation techniques.
In: Schlanger, S.O., et al., 1976, Initial Reports of the 
Deep Sea Drilling Project, vol. 33: Washington (U.S. 
Government Printing Office) pp. 931-958.

Explanatory Notes chapters, 1986 - present. In proceedings of 
the Ocean Drilling Program, Initial Reports.


EXPLANATION OF DATA ITEMS 

LEG - Number identifying the cruise.

SITE - Number identifying the site. A site is the position of 
a beacon around which holes are drilled.

HOLE - Letter identifying the hole.

CORE - Number identifying the core. Cores are numbered 
serially from the top of the hole downward.

CORETYPE - A letter code identifying the drill bit/coring 
method used to retrieve the core. The coretype codes are: 

B - Drill Bit
C - Center Bit
D - Positive Displacement
H - Hydraulic Piston Core
M - Miscellaneous
N - Downhole Mud Motor (Navidrill)
P - Pressure Core Barrel
R - Rotary
S - Side Wall Core
W - Wash Core
X - Extended Core Barrel

SECTION - A core is cut into 1.5 meter long sections that are 
numbered serially from the top of the core. A core with full 
recovery will have 7 sections and a core catcher and be 
approximately 9.8 meters long.

TOP_INTERVAL - Distance in centimeters from the top of the 
section to the top of the sample interval.

SUB_BOTTOM_DEPTH - Distance in meters from the seafloor to 
the top of the sample interval.

DENSITY - This is the calculated bulk density in g/cm3 
for a specific sample interval in the core section. 

COUNTS - The cumulative transmitted gamma ray count 
detected by the GRAPE apparatus over a specific sample 
interval. 

RUN_NUMBER - Each run of the MST is given a number which 
increments by one with every test.