MAGNETIC SUSCEPTIBILITY


INTRODUCTION

The Susceptibility data file contains the susceptibility 
measurements taken onboard JOIDES Resolution. A Bartington 
M.S.1 Magnetic Susceptibility meter on the ship can measure 
discrete samples or whole core sections passed through the 
instrument's sensor loop. These data files contain measurements made 
on whole core sections.


BIBLIOGRAPHY

Shipboard Scientific Party, 1987. Explanatory Notes. in 
Srivastava,S. P., Arthur, M. A., Clement, B. M., et al., 
Proc., Init. Repts.(Pt A), ODP, 105. 


EXPLANATION OF DATA ITEMS 

LEG - Number identifying the cruise.

SITE - Number identifying the site. A site is the position 
of a beacon around which holes are drilled. 

HOLE - Letter identifying the hole.

CORE - Number identifying the core. Cores are numbered 
serially from the top of the hole downward. 

CORETYPE - A letter code identifying the drill bit/coring 
method used to retrieve the core. The coretype codes are:

B - Drill Bit
C - Center Bit
D - Positive Displacement
H - Hydraulic Piston Core
M - Miscellaneous
N - Downhole Mud Motor (Navidrill)
P - Pressure Core Barrel
R - Rotary
S - Side Wall Core
W - Wash Core
X - Extended Core Barrel

SECTION - A core is cut into 1.5 meter long sections that 
are numbered serially from the top of the core. A core with 
full recovery will have 7 sections and a core catcher and be 
approximately 9.8 meters long. 

TOP_INTERVAL - The location of the top of a sample within a 
section in centimeters.

BOTTOM_INTERVAL - The location of the bottom of a sample 
within a section in centimeters.

SUB_BOTTOM_DEPTH - Distance in meters from the seafloor to 
the top of the sample interval.

SUSCEPTIBILITY - The value is in x10-6 cgs units and is 
volume corrected.

RUN_NUMBER - Each run of the MST is given a number which 
increments by one with every test.